| E/ECE/324/Rev.2/Add.120/Rev.1/Amend.2−E/ECE/TRANS/505/Rev.2/Add.120/Rev.1/Amend.2 |
| --- |
|  |  | 15 August 2012 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be fitted and/or be used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 120: Regulation No. 121

Revision 1 – Amendment 2

Supplement 6 to the original version of the Regulation - Date of entry into force: 26 July 2012

Uniform provisions concerning the approval of vehicles with regard to the location and identification of hand controls, tell-tales and indicators

UNITED NATIONS

Paragraph 2.5., amend to read:

"2.5.	"Tell-tale" means an optical signal that, when alight, indicates the actuation or deactivation of a device, a correct or defective functioning or condition, or a failure to function."

Table 1, amend to read:

"

| 2. | Headlamp passing beams | 1, 6, 13 | Control | No | - |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Tell-tale | Yes | Green |
| 3. | Headlamp driving beams |  | Control | No | - |
|  |  | 1, 13 | Tell-tale | Yes | Blue |

"

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.