| E/ECE/324 E/ECE/TRANS/505 |  | Rev.1/Add.43/Rev.2/Corr.1 |
| --- | --- | --- |
| 25 February 2009 |  |  |

# AGREEMENT

CONCERNING THE ADOPTION OF UNIFORM TECHNICAL PRESCRIPTIONS
FOR WHEELED VEHICLES, EQUIPMENT AND PARTS WHICH CAN BE FITTED
AND/OR BE USED ON WHEELED VEHICLES AND THE CONDITIONS FOR RECIPROCAL RECOGNITION OF APPROVALS GRANTED ON THE BASIS OF THESE PRESCRIPTIONS (/

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 43:  Regulation No. 44

## Revision 2 - Corrigendum 1

#### Corrigendum 1 to Revision 2 of the Regulation, subject of Depositary Notification C.N.16.2009.TREATIES-1 dated 15 January 2009 – Date of entry into force:  12 November 2008

Uniform provisions concerning the approval of restraining devices for child occupants of power-driven vehicles
("child restraint system")

_________

### UNITED NATIONS

Paragraph 7.1.4.4.1.1., amend to read:

"7.1.4.4.1.1.	Forward facing child restraints:  the head of the manikin shall not pass beyond the planes BA and DA as defined in Figure 1 below, except for booster seats when using the largest dummy P10 where the value in relation to DA plane is 840 mm."

-----

# Footnotes

(/	Former title of the Agreement:

Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.

GE.09-