E/ECE/324                         Rev.1/Add.53/Rev.2

E/ECE/TRANS/505

16 April 2004

# AGREEMENT

CONCERNING THE ADOPTION OF UNIFORM TECHNICAL PRESCRIPTIONS
FOR WHEELED VEHICLES, EQUIPMENT AND PARTS WHICH CAN BE FITTED
AND/OR BE USED ON WHEELED VEHICLES AND THE CONDITIONS FOR RECIPROCAL RECOGNITION OF APPROVALS GRANTED ON THE BASIS OF THESE PRESCRIPTIONS (/

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 53:  Regulation No. 54

## Revision 2

Incorporating all valid text up to:

#### Corrigendum 1 to Revision 1 of the Regulation subject of Depositary Notification C.N.438.1997.TREATIES-107 dated 14 November 1997

#### Supplement 10 to the original version of the Regulation - Date of entry into force:  24 May 1998

#### Supplement 11 to the original version of the Regulation - Date of entry into force:   7 February 1999

#### Supplement 12 to the original version of the Regulation - Date of entry into force:  29 December 2000

#### Supplement 13 to the original version of the Regulation - Date of entry into force:  29 March 2001

#### Supplement 14 to the original version of the Regulation - Date of entry into force:  21 February 2002 **/

#### Supplement 15 to the original version of the Regulation - Date of entry into force:  30 October 2003

Uniform provisions concerning the approval of pneumatic tyres for commercial vehicles and their trailers

_________

### UNITED NATIONS

Regulation No. 54

UNIFORM PROVISIONS CONCERNING THE APPROVAL OF PNEUMATIC TYRES

FOR COMMERCIAL VEHICLES AND THEIR TRAILERS

CONTENTS

REGULATION	Page

1.	Scope	5

2.	Definitions	5

3.	Markings	10

4.	Application for approval	12

5.	Approval	14

6.	Specifications	15

7.	Modification and extension of approval

of a tyre type	18

8.	Conformity of production	18

9.	Penalties for non-conformity of production	19

10.	Production definitely discontinued	19

11.	Names and addresses of technical services

responsible for conducting approval tests,

and of administrative departments	19

ANNEXES

Annex 1 	-	Communication concerning the approval or extension or refusal or withdrawal of approval or production definitely discontinued of a type of pneumatic tyre for motor vehicles pursuant to Regulation No. 54

Annex 2 	-	Arrangement of approval mark

Annex 3 	-	Arrangement of tyre markings

Annex 4	-	List of symbols of load-capacity indices

Annex 5	-	Tyre-size designation and dimensions: Part I - European tyres; Part II - United States tyres

Annex 6	-	Method of measuring pneumatic tyres

Annex 7	-	Procedure for load/speed endurance tests

Annex 7 - Appendix 1 - Endurance-test programme

Annex 7 - Appendix 2 - Relation between the pressure index and the units of pressure

Annex 8	-	Variation of load capacity with speed commercial vehicle tyres, radial and diagonal

_________

1.		SCOPE

This Regulation covers new pneumatic tyres designed primarily, but not only, for vehicles in categories M2, M3, N and O3 and O4. (/  However, it does not apply to tyre types identified by speed category symbols corresponding to speeds below 80 km/h.

2.		DEFINITIONS

For the purposes of this Regulation:

2.1.		"Type of pneumatic tyre" means a category of pneumatic tyres which do not differ in such essential respects as:

2.1.1.		The manufacturer;

2.1.2.		Tyre-size designation;

2.1.3.		Category of use;

2.1.4.		Structure (diagonal (bias-ply); radial);

2.1.5.		Speed category;

2.1.6.		Load-capacity indices; and

2.1.7.		Cross-section;

2.2.	Category of use:

2.2.1.	"Normal tyre" means a tyre intended for normal, everyday, on-road use;

2.2.2.	"Special use tyre" means a tyre intended for mixed use both on- and off-road or for other special duty.

2.2.3.		"Snow tyre" means a tyre whose tread pattern, tread compound or structure are primarily designed to achieve in snow conditions a performance better than that of a normal tyre with regard to its ability to initiate or maintain vehicle motion.

2.3.		"Structure" of a pneumatic tyre means the technical characteristics of the tyre's carcass.  A distinction is made between the following structures in particular:

2.3.1.		"Diagonal" or "bias-ply" describes a pneumatic-tyre structure in which the ply cords extend to the beads and are laid at alternate angles substantially less than 90° to the centreline of the tread;

2.3.2.		"Radial" describes a pneumatic-tyre structure in which the ply cords extend to the beads and are laid substantially at 90° to the centreline of the tread, the carcass being stabilized by an essentially inextensible circumferential belt.

2.4.		"Bead" means the part of a pneumatic tyre which is of such shape and structure as to fit the rim and to hold the tyre on it; /

2.5.		"Cord" means the strands forming the fabric of the plies in the pneumatic tyre; 1/

2.6.		"Ply" means a layer of rubber-coated parallel cords; 1/

2.7.		"Carcass" means that part of a pneumatic tyre other than the tread and the rubber sidewalls which, when inflated, bears the load; 1/

2.8.		"Tread" means that part of a pneumatic tyre which comes into contact with the ground, protects the carcass against mechanical damage and contributes to ground adhesion; 1/

2.9.		"Sidewall" means the part of a pneumatic tyre between the tread and the area designed to be covered by the rim flange; 1/

2.10.		"Lower sidewall" means the area included between the line of maximum section width of the tyre and the area designed to be covered by the rim flange; 1/

2.10.1.	However, in case of tyres identified by the "tyre to rim fitment configuration" (see paragraph 3.1.11.) symbol "A", it means the area of the tyre which is seating on the rim.

2.11.		"Tread groove" means the space between two adjacent ribs and/or blocks in the tread pattern; 1/

2.12.		"Section width (S)" means the linear distance between the outsides of the sidewalls of an inflated pneumatic tyre, excluding elevations due to labelling (marking), decoration or protective bands or ribs; 1/

2.13.		"Over-all width" means the linear distance between the outsides of the sidewalls of an inflated pneumatic tyre, including labelling (marking), decoration and protective bands or ribs; 1/

2.14.		"Section height (H)" means a distance equal to half the difference between the outer diameter of the tyre and the nominal rim diameter;

2.15.		"Nominal aspect ratio (Ra)" means one hundred times the number obtained by dividing the number expressing the section height (H) by the number expressing the nominal section width (S1), both dimensions expressed in the same units;

2.16.		"Outer diameter (D)" means the overall diameter of an inflated new pneumatic tyre; 1/

2.17.		"Tyre-size designation" means

2.17.1.		A designation showing:

2.17.1.1.	The nominal section width (S1).  This width must be expressed in mm, except in the case of types of tyre for which the size designation is shown in the first column of the tables in annex 5 to this Regulation;

2.17.1.2.	The nominal aspect ratio, except in the case of certain types of tyre for which the size designation is shown in the first column of the tables in annex 5 to this Regulation or, depending on the tyre design type, the nominal outer diameter expressed in mm;

2.17.1.3.	A conventional number "d" (the "d" symbol) denoting the nominal diameter of the rim and corresponding to its diameter expressed either in codes (number below 100) or in millimetres (numbers above 100).  Numbers corresponding to both types of measurement may be used together in the designation;

2.17.1.3.1.	The values of the "d" symbols expressed in millimetres are shown below:

| Nominal rim diameter code ("d" symbol) | Value of the "d" symbol expressed in mm |
| --- | --- |
| 8 9 10 11 12 13 14 | 203 229 254 279 305 330 356 |
| 15 16 17 18 19 | 381 406 432 457 482 |
| 20 21 22 24 25 | 508 533 559 610 635 |
| 14.5 16.5 17.5 19.5 20.5 22.5 24.5 26 28 30 | 368 419 445 495 521 572 622 660 711 762 |

2.17.1.4.	An indication of the tyre to rim fitment configuration when it differs from the standard configuration and is not already expressed by the symbol "d" denoting the nominal rim diameter code.

2.18.		"Nominal rim diameter (d)" means the diameter of the rim on which a tyre is designed to be mounted; 1/

2.19.		"Rim" means the support for a tyre-and-tube assembly, or for a tubeless tyre, on which support the tyre beads are seated; 1/

2.20.		"Theoretical rim" means a rim whose width would be equal to x times the nominal section width of a tyre; the value of x shall be specified by the manufacturer of the type;

2.21.		"Measuring rim" means the rim on which a tyre must be fitted for dimensional measurements;

2.22.		"Test rim" means the rim on which a tyre must be fitted for load/speed endurance testing;

2.23.		"Chunking" means the breaking away of pieces of rubber from the tread;

2.24.		"Cord separation" means the parting of the cords from their coating;

2.25.		"Ply separation" means the parting of adjacent plies;

2.26.		"Tread separation" means the pulling away of the tread from the carcass;

2.27.		"Load-capacity index" means one or two numbers which indicate the load the tyre can carry in single or in single and dual operation at the speed corresponding to the associated speed category and when operated in conformity with the requirements governing utilization specified by the manufacturer.  A type of pneumatic tyre can have either one or two sets of load capacity indices depending on whether or not the provisions of paragraph 6.2.5. are applied.  The list of these indices and their corresponding loads is given in annex 4;

2.28.		"Speed category" means:

2.28.1.		The speeds, indicated by a symbol, at which the tyre can carry the load indicated by the associated load-capacity index;

2.28.2.		The speed categories are as shown in the table below: /

| Speed-category symbol | Corresponding speed (km/h) |
| --- | --- |
| F G J K L M N P Q R S T U H | 80 90 100 110 120 130 140 150 160 170 180 190 200 210 |

2.29.		"Table load-capacity variation with speed" means:

The table, in annex 8, showing as a function of the load-capacity indices and nominal-speed-category symbols the load variations which a pneumatic tyre can withstand when used at speeds different from that conforming to its nominal-speed-category symbol.  The load variations do not apply in the case of the additional load capacity symbol and speed category obtained when the provisions of paragraph 6.2.5. are applied.

3.		MARKINGS

3.1.		Pneumatic tyres submitted for approval shall display on both sidewalls in the case of symmetrical tyres and at least on the outer sidewall in the case of asymmetrical tyres:

3.1.1.		The manufacturer's name or trade mark;

3.1.2.		The tyre-size designation as defined in paragraph 2.17. of this Regulation;

3.1.3.		An indication of the structure as follows:

3.1.3.1.	On diagonal (bias-ply) tyres: no indication, or the letter "D";

3.1.3.2.	On radial-ply tyres: the letter "R" placed in front of the rim-diameter marking and, optionally, the word "RADIAL";

3.1.4.		The speed-category symbol (or symbols);

3.1.4.1.	An indication of the tyre's nominal speed category in the form of the symbol prescribed in paragraph 2.28.2. above;

3.1.4.2.	An indication of a second speed category in cases where paragraph 6.2.5. below is applied;

3.1.5.		The inscription M+S or M.S or M&S in the case of a snow tyre;

3.1.6.		The load-capacity indices as defined in paragraph 2.27. of this Regulation;

3.1.7.		The word "TUBELESS" if the tyre is designed for use without an inner tube;

3.1.8.		The date of manufacture in the form of a group of four digits, the first two showing the week and the last two the year of manufacture.  However, this marking, which it is permissible to restrict to one sidewall, shall not be mandatory, on any tyre submitted submitted for approval, until two years after the date of entry into force of this Regulation; /

3.1.9.		In the case of tyres which can be regrooved, the symbol "(" at least 20 mm in diameter, or the word "REGROOVABLE", moulded into or on to each sidewall;

3.1.10.		An indication, by the "PSI" index, of the inflation pressure to be adopted for the load/speed endurance tests, as explained in annex 7, appendix 2.  However, this indication, which it is permissible to restrict to one sidewall, shall not be mandatory, on any tyre submitted for approval, until two years after the date of entry into force of this Regulation.

3.1.11.		In the case of tyres first approved after 1 March 2004 the identification referred to in paragraph 2.17.1.4. shall be placed only immediately after the rim diameter marking referred to in paragraph 2.17.1.3.

3.1.12.		The inscription "ET" or "ML" or "MPT" for "Special use tyres". /

3.1.13.	The suffix "C" or "LT" after the rim diameter marking referred to in paragraph 2.17.1.3., and, if applicable, after the tyre to rim fitment configuration referred to in paragraph 2.17.1.4.:

3.1.13.1.	this marking is optional in the case of tyres fitted on 5° drop centre rims, suitable for single and dual fitment, having a load capacity index in single lower or equal to 121 and destined for the equipment of motor vehicles.

3.1.13.2.	this marking is mandatory in the case of tyres fitted on 5° drop centre rims, suitable for single fitment only, having a load capacity index higher or equal to 122 and destined for the equipment of motor vehicles.

3.1.14.	The suffix "CP" after the rim diameter marking referred to in paragraph 2.17.1.3., and, if applicable, after the tyre to rim fitment configuration referred to in paragraph 2.17.1.4.  This marking is mandatory in the case of tyres fitted on 5° drop centre rims, having a load capacity index in single lower or equal to 121 and specifically designed for the equipment of motor caravans.

3.1.15.		The inscription "FRT" (free rolling tyres) in the case of tyres specifically designed for the equipment of trailers.

3.2.		Tyres shall exhibit a free space sufficiently large to accommodate an approval mark as shown in annex 2 to this Regulation.

3.3.		Annex 3 to this Regulation gives an example of an arrangement of the tyre markings.

3.4.		The markings referred to in paragraph 3.1. and the approval mark prescribed in paragraph 5.4. of this Regulation shall be moulded on to or into the tyres.  They shall be clearly legible and shall, except for the marking referred to in paragraph 3.1.1. above, be located on at least one lower sidewall.

3.4.1.		However, for tyres identified by the "tyre to rim fitment configuration" (see paragraph 3.1.11.) symbol "A", the markings may be placed anywhere on the sidewall of the tyre.

4.		APPLICATION FOR APPROVAL

4.1.		The application for approval of a type of pneumatic tyre shall be submitted by the holder of the manufacturer's name or trade mark or by his duly accredited representative.  It shall specify:

4.1.1.		The tyre-size designation as defined in paragraph 2.17. of this Regulation;

4.1.2.		The manufacturer's name or trade mark;

4.1.3.		The category of use (normal or special or snow);

4.1.4.		Structure:  diagonal (bias ply) or radial;

4.1.5.		The speed category;

4.1.6.		The load-capacity indices;

4.1.7.		Whether the tyre is intended to be used with or without an inner tube;

4.1.8.		The overall dimensions: overall section width and outer diameter;

4.1.9.		The factor "x" referred to in paragraph 2.20. above;

4.1.10.		The rims on which the tyre can be mounted;

4.1.11.		The measuring rim and test rim;

4.1.12.		The measuring pressure and test pressure index;

4.1.13.		The additional load/speed combinations in cases where paragraph 6.2.5. below is applied.

4.2.		The application for approval shall be accompanied (all in triplicate) by a sketch, or a representative photograph, which identify the tyre tread pattern and a sketch of the envelope of the inflated tyre mounted on the measuring rim showing the relevant dimensions (see paragraphs 6.1.1. and 6.1.2.) of the type submitted for approval.  It shall also be accompanied either by the test report issued by the approved test laboratory or by one or two samples of the tyre type, at the discretion of the competent authority.  Drawings or photographs of the side wall and tread of the tyre shall be submitted once production has been established, no later than one year after the date of issue of the type approval.

4.3.		The competent authority shall verify the existence of satisfactory arrangements for ensuring effective control of the conformity of production before type approval is granted.

4.4.		Where a tyre manufacturer submits application for type approval for a range of tyres, it is not considered necessary to carry out a load/speed test on every type of tyre in the range.  Worst case selection may be made at the discretion of the approval authority.

5.		APPROVAL

5.1.		If the type of pneumatic tyre submitted for approval in pursuance of this Regulation meets the requirements of paragraph 6 below, approval of that type of tyre shall be granted.

5.2.		An approval number shall be assigned to each type approved; its first two digits (at present 00 for the Regulation in its original form) shall indicate the series of amendments incorporating the most recent major technical amendments made to the Regulation at the time of issue of the approval.  The same Contracting Party may not assign the same number to another type of pneumatic tyre.

5.3.		Notice of approval or of refusal of approval of a type of pneumatic tyre pursuant to this Regulation shall be communicated to the Parties to the Agreement which apply this Regulation by means of a form conforming to the model in annex 1 to this Regulation.

5.4.		There shall be affixed, conspicuously, to every pneumatic tyre conforming to a type of tyre approved under this Regulation, in the space referred to in paragraph 3.2. above and in addition to the markings prescribed in paragraph 3.1. above, an international approval mark consisting of:

5.4.1.		a circle surrounding the letter "E" followed by the distinguishing number of the country which has granted approval; / and

5.4.2.		an approval number.

5.5.		The approval mark shall be clearly legible and be indelible.

5.6.		Annex 2 to this Regulation gives an example of the arrangement of the approval mark.

6.		SPECIFICATIONS

6.1.		Dimensions of tyres

6.1.1.		Section width of a tyre

6.1.1.1.	The section width shall be obtained by means of the following formula:

S = S1 + K (A - A1),

where:

S	is the "section width" expressed in millimetres and measured on the measuring rim;

S1	is "the nominal section width" in millimetres, as shown on the sidewall of the tyre in the tyre designation as prescribed;

A	is the width of the measuring rim in millimetres, as shown by the manufacturer in the descriptive note; and

A1	is the width of the theoretical rim in millimetres.

A1 shall be taken to equal S1 multiplied by the factor x as specified by the manufacturer, and K shall be taken to equal 0.4.

6.1.1.2.	However, for the existing types of tyres whose designation is given in the first column of the tables in annex 5 to this Regulation, the section width shall be deemed to be that given opposite the tyre designation in those tables.

6.1.1.3.	However, for tyres identified by the "tyre to rim fitment configuration" (see paragraph 3.1.11.) symbol "A", K shall be taken to equal 0.6.

6.1.2.		Outer diameter of a tyre

6.1.2.1.	The outer diameter of a tyre shall be obtained by means of the following formula:

D = d + 2H

where:

D	is the outer diameter expressed in millimetres;

d	is the conventional number defined in paragraph 2.17.1.3. above, expressed in millimetres;

S1	is the nominal section width in millimetres;

Ra	is the nominal aspect ratio;

H	is the nominal section height in millimetres and is equal to S1 x 0.01 Ra.

All as in the tyre designation shown on the sidewall of the tyre in conformity with the requirements of paragraph 3.4. above.

6.1.2.2.	However, for the existing types of tyres whose designation is given in the first column of the tables in annex 5 to this Regulation, the outer diameter shall be deemed to be that given opposite the tyre designation in those tables.

6.1.2.3.	However, for tyres identified by the "tyre to rim fitment configuration" (see paragraph 3.1.11.) symbol "A", the outer diameter shall be that specified in the tyre size designation as shown on the sidewall of the tyre.

6.1.3.		Method of measuring pneumatic tyres

The dimensions of pneumatic tyres shall be measured by the procedure described in annex 6 to this Regulation.

6.1.4.		Tyre section width specifications

6.1.4.1.	The overall width of a tyre may be less than the section width or widths determined pursuant to paragraph 6.1.1. above.

6.1.4.2.	It may exceed that value by 4 per cent in case of radial-ply tyres and by 8 per cent in the case of diagonal (bias-ply) tyres.  However, for tyres with nominal section width exceeding 305 mm intended for dual mounting (twinning), the value determined pursuant to paragraph 6.1.1. above shall not be exceeded by more than 2 per cent for radial-ply tyres with nominal aspect ratio higher than 60, or 4 per cent for diagonal (bias-ply) tyres.

6.1.4.3.	However, for tyres identified by the "tyre to rim fitment configuration" (see paragraph 3.1.11.) symbol "A", the overall width of the tyre, in the lower area of the tyre, equals the nominal width of the rim on which the tyre is mounted, as shown by the manufacturer in the descriptive note, increased by 27 mm.

6.1.5.		Tyre outer diameter specifications

The outer diameter of a tyre must not be outside the values Dmin and Dmax obtained from the following formulae:

Dmin = d + (2H x a)

Dmax = d + (2H x b)

where:

6.1.5.1.	For sizes listed in annex 5 and for tyres identified by the "tyre to rim fitment configuration" (see paragraph 3.1.11.) symbol "A", the nominal section height H is equal to:

H = 0.5 (D-d)	- for references see paragraph 6.1.2.1.

6.1.5.2.	For other sizes, not listed in annex 5

"H" and "d" are as defined in paragraph 6.1.2.1.

6.1.5.3.	Coefficients "a" and "b" are respectively:

6.1.5.3.1.	Coefficient "a" = .97

6.1.5.3.2.	Coefficient "b"			Radial		Diagonal

for normal use tyres		 1.04		  1.07

for special use tyres		 1.06		  1.09

6.1.5.3.3.	For snow tyres the outer diameter (Dmax) established in conformity with the above may be exceeded by 1 per cent.

6.2.		Load/speed endurance test

6.2.1.		Each type of pneumatic tyre shall undergo at least one load/speed endurance tests carried out by the procedure described in annex 7 to this Regulation.

6.2.2.		A tyre which, after undergoing the endurance test, does not exhibit any tread separation, ply separation, cord separation, chunking or broken cords shall be deemed to have passed the test.

6.2.3.		The outer diameter of the tyre, measured six hours after the load/speed endurance test, must not differ by more than  3.5 per cent from the outer diameter as measured before the test.

6.2.4.		Where application is made for the approval of a type of pneumatic tyre for the load/speed combinations given in the table in annex 8, the endurance test prescribed in paragraph 6.2.1. above need not be carried out for load and speed values other than the nominal values.

6.2.5.		Where application is made for the approval of a type of pneumatic tyre which has a load/speed combination in addition to the one that is subject to the variation of load with speed given in the table in annex 8, the endurance test prescribed in paragraph 6.2.1. above shall also be carried out on a second tyre of the same type at the additional load/speed combination.

7.		MODIFICATION AND EXTENSION OF APPROVAL OF A TYRE TYPE

7.1.		Every modification of a tyre type shall be notified to the administrative department which approved the tyre type.  That department may then either:

7.1.1.		Consider that the modifications made are unlikely to have an appreciable adverse effect and that in any case the tyre still meets the requirements; or

7.1.2.		Require a further test report from the technical service responsible for carrying out the tests.

7.2.		A modification of the tread pattern of the tyre shall not be considered to necessitate a repetition of the tests prescribed in paragraph 6 of this Regulation.

7.3.		Confirmation or refusal of approval, specifying the alterations, shall be communicated by the procedure specified in paragraph 5.3. above to the Parties to the Agreement which apply this Regulation.

7.4.		The competent authority issuing the extension of approval shall assign a series number for such an extension and inform thereof the other Parties to the 1958 Agreement applying this Regulation by means of a communication form conforming to the model in annex 1 to this Regulation.

8.	CONFORMITY OF PRODUCTION

The conformity of production procedures shall comply with those set out in the Agreement, Appendix 2 (E/ECE/324-E/ECE/TRANS/505/Rev. 2), with the following requirements:

8.1.	Tyres approved under this Regulation shall be so manufactured as to conform to the type approved, by meeting the requirements set forth in paragraph 6. above.

8.2.		The authority which has granted type approval may at any time verify the conformity control methods applied in each production facility.  For each production facility, the normal frequency of these verifications shall be once every two years.

9.		PENALTIES FOR NON-CONFORMITY OF PRODUCTION

9.1.		The approval granted in respect of a type of pneumatic tyre pursuant to this Regulation may be withdrawn if the requirement laid down in paragraph 8.1. above is not complied with or if the tyres taken from the series have failed to pass the tests prescribed in that paragraph.

9.2.		If a Party to the Agreement which applies this Regulation withdraws an approval it has previously granted, it shall forthwith so notify the other Contracting Parties applying this Regulation, by means of a communication form conforming to the model in annex 1 to this Regulation.

10.		PRODUCTION DEFINITELY DISCONTINUED

If the holder of an approval completely ceases to manufacture a type of pneumatic tyre approved in accordance with this Regulation, he shall so inform the authority which granted the approval.  Upon receiving the relevant communication that authority shall inform thereof the other Parties to the 1958 Agreement applying this Regulation by means of copies of the communication form conforming to the model in annex 1 to this Regulation.

11.		NAMES AND ADDRESSES OF TECHNICAL SERVICES RESPONSIBLE FOR CONDUCTING APPROVAL TESTS, AND OF ADMINISTRATIVE DEPARTMENTS

11.1.		The Parties to the Agreement which apply this Regulation shall communicate to the United Nations Secretariat the names and addresses of the technical services responsible for conducting approval tests and, where applicable, of the approved test laboratories and of the administrative departments which grant approval and to which forms certifying approval or refusal or withdrawal of approval, issued in other countries, are to be sent.

11.2.		The Parties to the Agreement which apply this Regulation may use laboratories of tyre manufacturers and may designate, as approved test laboratories, those among them which are situated on their territory or on the territory of another Party to the Agreement subject to a preliminary agreement to this procedure by the competent administrative department of the latter.

11.3.	Where a Party to the Agreement applies paragraph 11.2. above, it may, if it so desires, be represented at the tests by one or more persons of its choice.

Explanatory figure

(See paragraph 2. of the Regulation)

___________

Annex 1

COMMUNICATION

(Maximum format: A4 (210 x 297 mm))

concerning: 2/	APPROVAL GRANTED

APPROVAL EXTENDED

APPROVAL REFUSED

APPROVAL WITHDRAWN

PRODUCTION DEFINITELY DISCONTINUED

of a type of pneumatic tyre for motor vehicles pursuant to Regulation No. 54

Approval No. ............								Extension No. ...........

1.		Manufacturer's name or trade mark(s) on the tyre type

2.		Tyre type designation by the manufacturer

3.		Manufacturer's name and address

4.		If applicable, name and address of manufacturer's representative

5.		Summarized description:

5.1.		Size of tyre

5.2.		Category of use:  normal/special/snow 2/

5.3.		Structure:  diagonal (bias-ply)/radial 2/

5.4.		Speed category symbol:

5.4.1.	nominal

5.4.2.	additional (if applicable):

5.5.		Load-capacity indices:

5.5.1.	Corresponding to nominal speed: single ................... twinned (dual)

5.5.2.	Corresponding to additional speed: single ................. twinned (dual)

6.		Technical service and, where applicable, test laboratory approved for purposes of approval or of verification of conformity

7.		Date of report issued by that service

8.		Number of report issued by that service

9.		Reasons(s) of extension (if applicable)

10.		Any remarks:

11.		Place

12.		Date

13.		Signature

14.		Annexed to this communication is a list of documents in the approval file deposited at the administrative services having delivered the approval and which can be obtained upon request.

____________

______________

1/	Distinguishing number of the country which has granted/extended/refused/withdrawn approval (see approval provisions in the Regulation).

2/	Strike out what does not apply.

Annex 2

ARRANGEMENT OF APPROVAL MARK

a = 12 mm (min.)

The above approval mark affixed to a pneumatic tyre shows that the type of tyre concerned has been approved in the Netherlands (E 4) under approval number 002439.  The first two digits of the approval number indicate that the approval was granted in accordance with the requirements of Regulation No. 54 in its original form.

Note: The approval number must be placed close to the circle and either above or below the "E" or to left or right of that letter.  The digits of the approval number must be on the same side of the "E" and face in the same direction. The use of Roman numerals as approval numbers should be avoided so as to prevent any confusion with other symbols.

___________

Annex 3

ARRANGEMENT OF TYRE MARKINGS

|  | MINIMUM HEIGHTS OF MARKINGS (mm) |
| --- | --- |
|  | Tyres of nominal rim diameter ( 508 mm (Code 20) or of nominal section width ( 235 mm (Code 9) | Tyres of nominal rim diameter ( 508 mm (Code 20) or of nominal section width ( 235 mm (Code 9) |
| B | 6 | 9 |
| C | 4 |
| D | 6 |

1.	These markings, given as an example, define a pneumatic tyre:

Having a nominal section width of 255;

Having a nominal aspect ratio of 70;

Of radial-ply structure (R);

Having a nominal rim diameter of 572 mm, for which the symbol is 22.5;

Having load capacities of 3,150 kg when single and 2,900 kg when twinned (dual), corresponding respectively to the load indices 148 and 145 shown in annex 4 to this Regulation;

Having a reference speed of 100 km/h corresponding to speed category symbol: J

Classified in the category of use Snow: M+S

Able to be used additionally at 120 km/h (speed category symbol L) with a load capacity of 3,000 kg when single and 2,725 kg when twinned (dual), corresponding respectively to the load indices 145 and 143 shown in annex 4 to this Regulation

Capable of being fitted without inner tube: "TUBELESS"

Manufactured during the twenty-fifth week of the year 2003, and

Requiring to be inflated to 620 kPa for load/speed endurance tests, for which the PSI symbol is 90.

2.	In the particular case of tyres having a tyre to rim fitment configuration "A", the marking shall be in the form of the following example:

235-700 R 450A     where:

235 is the nominal section width in mm

700 is the outer diameter expressed in mm

R is an indication of the structure of the tyre -see paragraph 3.1.3. of this Regulation

450 is the nominal diameter of the rim expressed in mm

A is the tyre to rim fitment configuration.

The marking of the load index, speed category symbol, date of manufacture and other markings, shall be as given in example 1 above.

3.	The positioning and order of the markings constituting the tyre designation shall be the following:

a)	The tyre-size designation as defined in paragraph 2.17. of this Regulation shall be grouped as shown in  above examples: 255/70 R 22.5 or 235-700 R 450A;

(b)	The service description comprising the load index/indices and the speed symbol shall be placed immediately after the tyre size designation as defined in paragraph 2.17 of this Regulation;

(c)	The symbols "TUBELESS" and "M+S" or "FRT" or "MPT" (and equivalents) may be at a distance from the tyre size designation

(d)	If paragraph 6.2.5. of this Regulation is applied, the additional load-capacity indices and speed-category symbol must be shown inside a circle near the nominal load-capacity indices and speed-category-symbol appearing on the tyre sidewall.

___________

Annex 4

LIST OF SYMBOLS OF LOAD-CAPACITY INDICES

| Load-capacity index | Corresponding maximum mass to be carried (kg) |
| --- | --- |
| 60 61 62 63 64 65 66 67 68 69 70 71 72 73 74 75 76 77 78 79 80 81 82 83 84 85 86 87 88 89 90 91 92 93 94 95 96 97 98 99 100 101 102 103 104 105 106 107 108 109 110 111 112 113 114 115 116 117 118 119 | 250 257 265 272 280 290 300 307 315 325 335 345 355 365 375 387 400 412 425 437 450 462 475 487 500 515 530 545 560 580 600 615 630 650 670 690 710 730 750 775 800 825 850 875 900 925 950 975 1 000 1 030 1 060 1 090 1 120 1 150 1 180 1 215 1 250 1 285 1 320 1 360 |

| Load-capacity index | Corresponding maximum mass to be carried (kg) |
| --- | --- |
| 120 121 122 123 124 125 126 127 128 129 130 131 132 133 134 135 136 137 138 139 140 141 142 143 144 145 146 147 148 149 | 1 400 1 450 1 500 1 550 1 600 1 650 1 700 1 750 1 800 1 850 1 900 1 950 2 000 2 060 2 120 2 180 2 240 2 300 2 360 2 430 2 500 2 575 2 650 2 725 2 800 2 900 3 000 3 075 3 150 3 250 |

| Load-capacity index | Corresponding maximum mass to be carried (kg) |
| --- | --- |
| 150 151 152 153 154 155 156 157 158 159 160 161 162 163 164 165 166 167 168 169 170 171 172 173 174 175 176 177 178 179 | 3 350 3 450 3 550 3 650 3 750 3 875 4 000 4 125 4 250 4 375 4 500 4 625 4 750 4 875 5 000 5 150 5 300 5 450 5 600 5 800 6 000 6 150 6 300 6 500 6 700 6 900 7 100 7 300 7 500 7 750 |

| Load-capacity index | Corresponding maximum mass to be carried (kg) |
| --- | --- |
| 180 181 182 183 184 185 186 187 188 189 190 191 192 193 194 195 196 197 198 199 200 | 8 000 8 250 8 500 8 750 9 000 9 250 9 500 9 750 10 000 10 300 10 600 10 900 11 200 11 500 11 800 12 150 12 500 12 850 13 200 13 600 14 000 |

___________

Annex 5

TYRE-SIZE DESIGNATION AND DIMENSIONS

PART I

EUROPEAN TYRES

Table A

CODE DESIGNATED SIZES MOUNTED ON 5° TAPERED RIMS OR FLAT BASE RIMS.

RADIAL AND DIAGONAL CONSTRUCTIONS

| Tyre Size Designation (+) | Measuring Rim Width Code | Nominal Rim Diameter d (mm) | Outer Diameter D (mm) | Section Width S (mm) |
| --- | --- | --- | --- | --- |
|  |  |  | Radial | Diagonal | Radial | Diagonal |
| Std. series 4.00R8 (*) 4.00R10(*) 4.00R12(*) 4.50R8 (*) 4.50R10(*) 4.50R12(*) 5.00R8 (*) 5.00R10(*) 5.00R12(*) 6.00R9 6.00R14C 6.00R16(*) 6.50R10 6.50R14C 6.50R16(*) 6.50R20(*) 7.00R12 7.00R14C 7.00R15(*) 7.00R16C 7.00R16 7.00R20 7.50R10 7.50R14C 7.50R15(*) 7.50R16(*) 7.50R17(*) 7.50R20 8.25R15 8.25R16 8.25R17 8.25R20 | 2.50 3.00 3.00 3.50 3.50 3.50 3.00 3.50 3.50 4.00 4.50 4.50 5.00 5.00 4.50 5.00 5.00 5.00 5.00 5.50 5.50 5.50 5.50 5.50 6.00 6.00 6.00 6.00 6.50 6.50 6.50 6.50 | 203 254 305 203 254 305 203 254 305 229 356 406 254 356 406 508 305 356 381 406 406 508 254 356 381 406 432 508 381 406 432 508 | 414 466 517 439 490 545 467 516 568 540 626 728 588 640 742 860 672 650 746 778 784 892 645 686 772 802 852 928 836 860 886 962 | 414 466 517 439 490 545 467 516 568 540 625 730 588 650 748 - 672 668 752 778 774 898 645 692 772 806 852 928 836 860 895 970 | 107 108 108 125 125 125 132 134 134 160 158 170 177 170 176 181 192 180 197 198 198 198 207 195 212 210 210 210 230 230 230 230 | 107 108 108 125 125 128 132 134 137 160 158 170 177 172 176 - 192 182 198 198 198 198 207 192 212 210 210 213 234 234 234 234 |

Table A - (cont'd)

| Tyre size designation (+) | Measuring rim width code | Nominal rim diameter d (mm) | Outer diameter D (mm) | Section Width S (mm) |
| --- | --- | --- | --- | --- |
|  |  |  | Radial | Diagonal | Radial | Diagonal |
| 9.00R15 9.00R16(*) 9.00R20 10.00R15 10.00R20 10.00R22 11.00R16 11.00R20 11.00R22 11.00R24 12.00R20 12.00R22 12.00R24 13.00R20 14.00R20 14.00R24 16.00R20 80 Series 12/80 R 20 13/80 R 20 14/80 R 20 14/80 R 24 14.75/80 R 20 15.5/80 R 20 | 6.00 6.50 7.00 7.50 7.50 7.50 6.50 8.00 8.00 8.00 8.50 8.50 8.50 9.00 10.00 10.00 13.00 8.50 9.00 10.00 10.00 10.00 10.00 | 381 406 508 381 508 559 406 508 559 610 508 559 610 508 508 610 508 508 508 508 610 508 508 | 840 912 1018 918 1052 1102 980 1082 1132 1182 1122 1174 1226 1176 1238 1340 1370 1008 1048 1090 1192 1124 1158 | 840 900 1012 918 1050 1102 952 1080 1130 1180 1120 1174 1220 1170 1238 1340 1370 - - - - - - | 249 246 258 275 275 275 279 286 286 286 313 313 313 336 370 370 446 305 326 350 350 370 384 | 249 252 256 275 275 275 272 291 291 291 312 312 312 342 375 375 446 - - - - - - |
| Wide Base Tyres for Multipurpose Trucks |
| 7.50 R 18 MPT 10.5 R 18 MPT 10.5 R 20 MPT 12.5 R 18 MPT 12.5 R 20 MPT 14.5 R 20 MPT 14.5 R 24 MPT | 5.50 9 9 11 11 11 11 | 457 457 508 457 508 508 610 | 885 905 955 990 1040 1095 1195 | 276 276 330 330 362 362 | 208 270 270 325 325 355 355 |

(+)	Tyres in diagonal construction are identified by an hyphen in place of the letter 'R'
(e.g. 5.00-8).

(*)	The tyre size designation may be supplemented with the letter 'C' (e.g. 6.00-16C).

Table B

CODE DESIGNATED SIZES MOUNTED ON 15° TAPERED RIMS - RADIAL

| Tyre size designation | Measuring rim width code | Nominal rim diameter d (mm) | Outer diameter D (mm) | Section Width S (mm) |
| --- | --- | --- | --- | --- |
| 7 R 17.5 (*) 7 R 19.5 8 R 17.5 (*) 8 R 19.5 8 R 22.5 8.5 R 17.5 9 R 17.5 9 R 19.5 9 R 22.5 9.5 R 17.5 9.5 R 19.5 10 R 17.5 10 R 19.5 10 R 22.5 11 R 22.5 11 R 24.5 12 R 22.5 13 R 22.5 15 R 19.5 15 R 22.5 16.5 R 19.5 16.5 R 22.5 18 R 19.5 18 R 22.5 70 Series 10/70 R 22.5 11/70 R 22.5 12/70 R 22.5 13/70 R 22.5 | 5.25 5.25 6.00 6.00 6.00 6.00 6.75 6.75 6.75 6.75 6.75 7.50 7.50 7.50 8.25 8.25 9.00 9.75 11.75 11.75 13.00 13.00 14.00 14.00 7.50 8.25 9.00 9.75 | 445 495 445 495 572 445 445 495 572 445 495 445 495 572 572 622 572 572 495 572 495 572 495 572 572 572 572 572 | 752 800 784 856 936 802 820 894 970 842 916 858 936 1020 1050 1100 1084 1124 998 1074 1046 1122 1082 1158 928 962 1000 1033 | 185 185 208 208 208 215 230 230 230 240 240 254 254 254 279 279 300 320 387 387 425 425 457 457 254 279 305 330 |

(*)	The tyre size designation may be supplemented with the letter 'C' (e.g. 7 R 17.5C).

Table C

TYRES FOR LIGHT COMMERCIAL VEHICLES - RADIAL AND DIAGONAL CONSTRUCTIONS

| Tyre size designation (+) | Measuring rim width code | Nominal rim diameter d (mm) | Outer diameter D (mm) | Section Width S (mm) |
| --- | --- | --- | --- | --- |
|  |  |  | Radial | Diagonal | Radial | Diagonal |
| Metric Designated |
| 145 R 10 C 145 R 12 C 145 R 13 C 145 R 14 C 145 R 15 C 155 R 12 C 155 R 13 C 155 R 14 C 165 R 13 C 165 R 14 C 165 R 15 C 175 R 13 C 175 R 14 C 175 R 16 C 185 R 13 C 185 R 14 C 185 R 15 C 185 R 16 C 195 R 14 C 195 R 15 C 195 R 16 C 205 R 14 C 205 R 15 C 205 R 16 C 215 R 14 C 215 R 15 C 215 R 16 C 245 R 16 C 17 R 15 C 17 R 380 C 17 R 400 C 19 R 400 C | 4.00 4.00 4.00 4.00 4.00 4.50 4.50 4.50 4.50 4.50 4.50 5.00 5.00 5.00 5.50 5.50 5.50 5.50 5.50 5.50 5.50 6.00 6.00 6.00 6.00 6.00 6.00 7.00 5.00 5.00 150 mm 150 mm | 254 305 330 356 381 305 330 356 330 356 381 330 356 406 330 356 381 406 356 381 406 356 381 406 356 381 406 406 381 381 400 400 | 492 542 566 590 616 550 578 604 596 622 646 608 634 684 624 650 674 700 666 690 716 686 710 736 700 724 750 798 678 678 698 728 | - - - - - - - - - - - - - - - - - - - - - - - - - - - 798 - - - - | 147 147 147 147 147 157 157 157 167 167 167 178 178 178 188 188 188 188 198 198 198 208 208 208 218 218 218 248 178 178 186 200 | - - - - - - - - - - - - - - - - - - - - - - - - - - - 248 - - - - |
| Code Designated |
| 5.60 R 12 C 6.40 R 13 C 6.70 R 13 C 6.70 R 14 C 6.70 R 15 C | 4.00 5.00 5.00 5.00 5.00 | 305 330 330 356 381 | 570 648 660 688 712 | 572 640 662 688 714 | 150 172 180 180 180 | 148 172 180 180 180 |

(+)	Tyres in diagonal construction are identified by an hyphen in place of the letter 'R'
(e.g. 145-10 C).

Table D

TYRES FOR SPECIAL APPLICATIONS - RADIAL AND DIAGONAL CONSTRUCTION

| Tyre size designation (+) | Measuring rim width code | Nominal rim diameter d (mm) | Outer diameter D (mm) | Section Width S (mm) |
| --- | --- | --- | --- | --- |
| Code Designated |
| 15x4 1/2-8 16x6-8 18x7 18x7-8 21x8-9 21x4 22x4 1/2 23x5 23x9-10 25x6 27x10-12 28x9-15 | 3.25 4.33 4.33 4.33 6.00 2.32 3.11 3.75 6.50 3.75 8.00 7.00 | 203 203 203 203 229 330 330 330 254 330 305 381 | 385 425 462 462 535 565 595 635 595 680 690 707 | 122 152 173 173 200 113 132 155 225 170 255 216 |
| Metric designated |
| 200-15 250-15 300-15 | 6.50 7.50 8.00 | 381 381 381 | 730 735 840 | 205 250 300 |

(+)	Tyres in radial construction are identified by the letter 'R' in place of the hyphen '-' (e.g. 15x4 1/2 R 8).

PART II

UNITED STATES TYRES

-	Tolerances shown at the bottom of the tables apply in place of those shown in paras. 6.1.4.2. and 6.1.5.3.

-	Outer diameters are listed for the various categories of use: Normal, Snow, Special.

Table A

TYRES FOR LIGHT COMMERCIAL VEHICLES (LT TYRES)

DIAGONAL AND RADIAL

| Tyre size designation 1/ | Measuring rim width code | Nominal rim diameter d(mm) | Outer diameter D (mm) 2/ Normal Snow | Section width S (mm) 3/ |
| --- | --- | --- | --- | --- |
| 6.00-16LT | 4.50 | 406 | 732 | 743 | 173 |
| 6.50-16LT | 4.50 | 406 | 755 | 767 | 182 |
| 6.70-16LT | 5.00 | 406 | 722 | 733 | 191 |
| 7.00-13LT | 5.00 | 330 | 647 | 658 | 187 |
| 7.00-14LT | 5.00 | 356 | 670 | 681 | 187 |
| 7.00-15LT | 5.50 | 381 | 752 | 763 | 202 |
| 7.00-16LT | 5.50 | 406 | 778 | 788 | 202 |
| 7.10-15LT | 5.00 | 381 | 738 | 749 | 199 |
| 7.50-15LT | 6.00 | 381 | 782 | 794 | 220 |
| 7.50-16LT | 6.00 | 406 | 808 | 819 | 220 |
| 8.25-16LT | 6.50 | 406 | 859 | 869 | 241 |
| 9.00-16LT | 6.50 | 406 | 890 | 903 | 257 |
| G78-15LT | 6.00 | 381 | 711 | 722 | 212 |
| H78-15LT | 6.00 | 381 | 727 | 739 | 222 |
| L78-15LT | 6.50 | 381 | 749 | 760 | 236 |
| L78-16LT | 6.50 | 406 | 775 | 786 | 236 |
| 7-14.5LT 4/ | 6.00 | 368 | 677 |  | 185 |
| 8-14.5LT 4/ | 6.00 | 368 | 707 |  | 203 |
| 9-14.5LT 4/ | 7.00 | 368 | 711 |  | 241 |
| 7-17.5LT | 5.25 | 445 | 758 | 769 | 189 |
| 8-17.5LT | 5.25 | 445 | 788 | 799 | 199 |

1/	Tyres in Radial construction are identified by the letter "R" in place of "-"
(e.g. 6.00 R 16LT).

2/	Coefficient "b" for the calculation of Dmax: 1.08.

3/	Overall width may exceed this value up to +8 per cent.

4/	The suffix "MH"' may replace "LT" in the tyre size designation (e.g. 7-14.5 MH).

Table B

TYRES FOR LIGHT COMMERCIAL VEHICLES (HIGH FLOTATION TYRES)

DIAGONAL AND RADIAL

| Tyre size | Measuring | Nominal | Outer diameter | Section width |
| --- | --- | --- | --- | --- |
| designation | rim width | rim | D (mm) 2/ |  |
|  | code | diameter |  |  | S (mm) |
| 1/ |  | d (mm) | Normal | Snow | 3/ |
| 9-15LT | 8.00 | 381 | 744 | 755 | 254 |
| 10-15LT | 8.00 | 381 | 773 | 783 | 264 |
| 11-15LT | 8.00 | 381 | 777 | 788 | 279 |
| 24x7.50-13LT | 6 | 330 | 597 | 604 | 191 |
| 27x8.50-14LT | 7 | 356 | 674 | 680 | 218 |
| 28x8.50-15LT | 7 | 381 | 699 | 705 | 218 |
| 29x9.50-15LT | 7.5 | 381 | 724 | 731 | 240 |
| 30x9.50-15LT | 7.5 | 381 | 750 | 756 | 240 |
| 31x10.50-15LT | 8.5 | 381 | 775 | 781 | 268 |
| 31x11.50-15LT | 9 | 381 | 775 | 781 | 290 |
| 31x13.50-15LT | 11 | 381 | 775 | 781 | 345 |
| 31x15.50-15LT | 12 | 381 | 775 | 781 | 390 |
| 32x11.50-15LT | 9 | 381 | 801 | 807 | 290 |
| 33x12.50-15LT | 10 | 381 | 826 | 832 | 318 |
| 35x12.50-15LT | 10 | 381 | 877 | 883 | 318 |
| 37x12.50-15LT | 10 | 381 | 928 | 934 | 318 |
| 37x14.50-15LT | 12 | 381 | 928 | 934 | 372 |
| 8.00-16.5LT | 6.00 | 419 | 720 | 730 | 203 |
| 8.75-16.5LT | 6.75 | 419 | 748 | 759 | 222 |
| 9.50-16.5LT | 6.75 | 419 | 776 | 787 | 241 |
| 10-16.5LT | 8.25 | 419 | 762 | 773 | 264 |
| 12-16.5LT | 9.75 | 419 | 818 | 831 | 307 |
| 30x9.50-16.5LT | 7.50 | 419 | 750 | 761 | 240 |
| 31x10.50-16.5LT | 8.25 | 419 | 775 | 787 | 266 |
| 33x12.50-16.5LT | 9.75 | 419 | 826 | 838 | 315 |
| 37x12.50-16.5LT | 9.75 | 419 | 928 | 939 | 315 |
| 37x14.50-16.5LT | 11.25 | 419 | 928 | 939 | 365 |
| 33x9.50 R15LT | 7.50 | 381 | 826 | 832 | 240 |
| 35x12.50 R16.5LT | 10.00 | 419 | 877 | 883 | 318 |
| 37x12.50 R17LT | 10.00 | 432 | 928 | 934 | 318 |

___________________

1/	Tyres in Radial construction are identified by the letter "R" in place of "-"
(e.g. 24x7.50 R 13LT).

2/	Coefficient 'b' for the calculation of Dmax: 1.07.

3/	Overall width may exceed this value up to +7 per cent.

Table C

CODE DESIGNATED TYRES MOUNTED ON 5° TAPERED OR FLAT BASE RIMS

DIAGONAL AND RADIAL

| Tyre size | Measuring | Nominal | Outer diameter |  | Section width |
| --- | --- | --- | --- | --- | --- |
| designation | rim width | rim | D (mm) 2/ |  |  |
|  | code | diameter | Normal |  |  | S (mm) |
| 1/ |  | d (mm) | (a) | (b) | Snow | 3/ |
| 6.50-20 | 5 | 508 | 878 |  | 893 | 184 |
| 7.00-15TR | 5.5 | 381 | 777 |  | 792 | 199 |
| 7.00-18 | 5.5 | 457 | 853 |  | 868 | 199 |
| 7.00-20 | 5.5 | 508 | 904 |  | 919 | 199 |
| 7.50-15TR | 6 | 381 | 808 |  | 825 | 215 |
| 7.50-17 | 6 | 432 | 859 |  | 876 | 215 |
| 7.50-18 | 6 | 457 | 884 |  | 901 | 215 |
| 7.50-20 | 6 | 508 | 935 |  | 952 | 215 |
| 8.25-15TR | 6.5 | 381 | 847 | 855 | 865 | 236 |
| 8.25-20 | 6.5 | 508 | 974 | 982 | 992 | 236 |
| 9.00-15TR | 7 | 381 | 891 | 904 | 911 | 259 |
| 9.00-20 | 7 | 508 | 1019 | 1031 | 1038 | 259 |
| 10.00-15TR | 7.5 | 381 | 927 | 940 | 946 | 278 |
| 10.00-20 | 7.5 | 508 | 1054 | 1067 | 1073 | 278 |
| 10.00-22 | 7.5 | 559 | 1104 | 1118 | 1123 | 278 |
| 11.00-20 | 8 | 508 | 1085 | 1099 | 1104 | 293 |
| 11.00-22 | 8 | 559 | 1135 | 1150 | 1155 | 293 |
| 11.00-24 | 8 | 610 | 1186 | 1201 | 1206 | 293 |
| 11.50-20 | 8 | 508 | 1085 | 1099 | 1104 | 296 |
| 12.00-20 | 8.5 | 508 | 1125 |  | 1146 | 315 |
| 12.00-24 | 8.5 | 610 | 1226 |  | 1247 | 315 |
| 14.00-20 | 10 | 508 | 1241 |  | 1266 | 375 |
| 14.00-24 | 10 | 610 | 1343 |  | 1368 | 375 |

1/	Tyres in Radial construction are identified by the letter "R" in place of "-".(e.g. 6.50 R 20).

2/	Coefficient 'b' for the calculation of Dmax : 1.06 . Category of use:   Normal Service tyres: (a) Highway tread   (b) Heavy tread

3/	Overall width may exceed this value up to +6 per cent.

Table D

CODE DESIGNATED TYRES FOR SPECIAL SERVICES

DIAGONAL AND RADIAL

| Tyre size | Measuring | Nominal | Outer diameter | Section width |
| --- | --- | --- | --- | --- |
| designation | rim width | rim | D (mm) 1/ |  |
|  | code | diameter |  |  | S (mm) |
|  |  | d (mm) | (a) | (b) | 2/ |
| 10.00-20ML | 7.5 | 508 | 1073 | 1099 | 278 |
| 11.00-22ML | 8 | 559 | 1155 | 1182 | 293 |
| 13.00-24ML | 9 | 610 | 1302 |  | 340 |
| 14.00-20ML | 10 | 508 | 1266 |  | 375 |
| 14.00-24ML | 10 | 610 | 1368 |  | 375 |
| 15-19.5ML | 11.75 | 495 | 1019 |  | 389 |
| 24 R 21 | 18 | 533 | 1372 | - | 610 |

1/	Coefficient "b" for the calculation of Dmax : 1.06.

Category of use:  special  (a) Traction tread  (b) Heavy tread

2/	Overall width may exceed this value up to +8 per cent.

Table E

CODE DESIGNATED TYRES MOUNTED ON 15° TAPERED RIMS

DIAGONAL AND RADIAL

| Tyre size | Measuring | Nominal | Outer diameter |  | Section width |
| --- | --- | --- | --- | --- | --- |
| designation | rim width | rim | D (mm) 2/ |  |  |
|  | code | diameter | Normal |  |  | S (mm) |
| 1/ |  | d (mm) | (a) | (b) | Snow | 3/ |
| 8-19.5 | 6.00 | 495 | 859 |  | 876 | 203 |
| 8-22.5 | 6.00 | 572 | 935 |  | 952 | 203 |
| 9-22.5 | 6.75 | 572 | 974 | 982 | 992 | 229 |
| 10-22.5 | 7.50 | 572 | 1019 | 1031 | 1038 | 254 |
| 11-22.5 | 8.25 | 572 | 1054 | 1067 | 1073 | 279 |
| 11-24.5 | 8.25 | 622 | 1104 | 1118 | 1123 | 279 |
| 12-22.5 | 9.00 | 572 | 1085 | 1099 | 1104 | 300 |
| 12-24.5 | 9.00 | 622 | 1135 | 1150 | 1155 | 300 |
| 12.5-22.5 | 9.00 | 572 | 1085 | 1099 | 1104 | 302 |
| 12.5-24.5 | 9.00 | 622 | 1135 | 1150 | 1155 | 302 |
| 14-17.5 | 10.50 | 445 | 907 |  | 921 | 349 (-) |
| 15-19.5 | 11.75 | 495 | 1005 |  | 1019 | 389 (-) |
| 15-22.5 | 11.75 | 572 | 1082 |  | 1095 | 389 (-) |
| 16.5-22.5 | 13.00 | 572 | 1128 |  | 1144 | 425 (-) |
| 18-19.5 | 14.00 | 495 | 1080 |  | 1096 | 457 (-) |
| 18-22.5 | 14.00 | 572 | 1158 |  | 1172 | 457 (-) |

1/	Tyres in Radial construction are identified by the letter "R" in place of "-" (e.g. 8R19.5).

2/	Coefficient "b" for the calculation of Dmax : 1.05.

Category of use:  Normal Service tyres:   (a) Highway tread  (b) Heavy tread

3/	Overall width may exceed this value up to +6 per cent

(-)Overall width may exceed this value up to +5 per cent.

_____________

Annex 6

METHOD OF MEASURING PNEUMATIC TYRES

1.	The tyre is mounted on the measuring rim specified by the manufacturer pursuant to paragraph 4.1.11. of this Regulation and is inflated to a pressure specified by the manufacturer pursuant to paragraph 4.1.12. of this Regulation.

2.	The tyre fitted on its rim is conditioned to the ambient temperature of the laboratory for at least 24 hours.

3.	The pressure is readjusted to the value specified in paragraph 1. above.

4.	The overall width is measured by caliper at six equally-spaced points, account being taken of the thickness of the protective ribs or bands.  The highest measurement so obtained is taken as the overall width.

5.	The outer diameter is calculated from the maximum circumference.

____________

Annex 7

PROCEDURE FOR LOAD/SPEED ENDURANCE TESTS

1.	Preparing the tyre

1.1.	Mount a new tyre on the test rim specified by the manufacturer pursuant to paragraph 4.1.11. of this Regulation.

1.2.	Use a new inner tube or combination of inner tube, valve and flap (as required) when testing tyres with inner tubes.

1.3.	Inflate the tyre to the pressure corresponding to the pressure index specified by the manufacturer pursuant to paragraph 4.1.12. of this Regulation.

1.4.	Condition the tyre-and-wheel assembly at test-room temperature for not less than three hours.

1.5.	Readjust the tyre pressure to that specified in paragraph 1.3. above.

2.	Test procedure

2.1.	Mount the tyre-and-wheel assembly on the test axle and press it against the outer face of a smooth power-driven test drum 1.70 m ( 1 per cent in diameter having a surface at least as wide as the tyre tread.

2.2.	Apply to the test axle a series of test loads expressed in per cent of the load indicated, in annex 4 to this Regulation, opposite the load index engraved on the sidewall of the tyre, in accordance with the test programme below.  Where the tyre has load-capacity indices for both single and twinned utilization, the reference load for single utilization shall be taken as the basis for the test loads.

2.2.1.	In the case of  tyres with a speed category symbol above P, test procedures are as specified in paragraph 3.

2.2.2.	For all other tyre types, the endurance test programme is shown in appendix 1 to this annex.

2.3.	The tyre pressure must not be corrected throughout the test and the test load must be kept constant throughout each of the three test stages.

2.4.	During the test the temperature in the test-room must be maintained at between 20°C and 30°C or at a higher temperature if the manufacturer so agrees.

2.5.	The endurance-test programme shall be carried out without interruption.

3.	Load/speed test programme for tyre with speed category symbol Q and above

3.1.	This programme applies to:

3.1.1.	all tyres marked with load capacity index in single 121 or less.

3.1.2.	tyres marked with load capacity index in single 122 and above and with the additional marking "C", or "LT", referred to in paragraph 3.1.13. of this Regulation.

3.2.	Load placed on the wheel as a percentage of the load corresponding to the load index:

3.2.1.	90% when tested on a test drum 1.70 m ( 1 per cent in diameter;

3.2.2.	92% when tested on a test drum 2.0 m ( 1 per cent in diameter.

3.3.	Initial test speed: speed corresponding to the speed category symbol less 20 km/h;

3.3.1.	Time to reach the initial test speed 10 min.

3.3.2.	Duration of the first step = 10 min.

3.4.	Second test speed: speed corresponding to the speed category symbol less 10 km/h;

3.4.1.	Duration of the second step = 10 min.

3.5.	Final test speed: speed corresponding to the speed category symbol:

3.5.1.	Duration of the final step = 30 min.

3.6.	Total test duration: 1 h.

4.	Equivalent test methods

If a method other than that described in paragraph 2. above is used, its equivalence must be demonstrated.

__________

Annex 7 - Appendix 1

ENDURANCE-TEST PROGRAMME

| Load index | Tyre speed category | Test-drum speed | Load placed on the wheel as a percentage of the load corresponding to the load index |
| --- | --- | --- | --- |
|  |  | Radial-ply min-1 | Diagonal (bias-ply) min-1 | 7 h. | 16 h. | 24 h. |
| 122 or more | F G J K L M | 100 125 150 175 200 225 | 100 100 125 150 - - | 66% | 84% | 101% |
| 121 or less | F G J K | 100 125 150 175 | 100 125 150 175 |  |  |  |
|  | L M N P | 200 250 275 300 | 175 200 - - | 70% 4 h. 75% 75% 75% | 88% 6 h. 97% 97% 97% | 106% 114% 114% 114% |

Notes:

(1)	"Special-use" tyres (see paragraph 2.1.3. of the Regulation) should be tested at a speed equal to 85 per cent of the speed prescribed for equivalent normal tyres.

(2)	Tyres with load index 121 or more, speed categories N or P and the additional marking "LT", or "C", referred to in paragraph 3.1.13. of this Regulation, shall be tested with the same programme as specified in the above table for tyres with load index 121 or less.

____________

Annex 7 - Appendix 2

RELATION BETWEEN THE PRESSURE INDEX AND THE UNITS OF PRESSURE

| Pressure Index ("PSI") | Bar | kPa |
| --- | --- | --- |
| 20 25 30 35 40 45 50 55 60 65 70 75 80 85 90 95 100 105 110 115 120 125 130 135 140 145 150 ... | 1.4 1.7 2.1 2.4 2.8 3.1 3.4 3.8 4.1 4.5 4.8 5.2 5.5 5.9 6.2 6.6 6.9 7.2 7.6 7.9 8.3 8.6 9.0 9.3 9.7 10.0 10.3 ... | 140 170 210 240 280 310 340 380 410 450 480 520 550 590 620 660 690 720 760 790 830 860 900 930 970 1000 1030 ... |

___________

Annex 8

VARIATION OF LOAD CAPACITY WITH SPEED COMMERCIAL VEHICLES TYRES

RADIAL AND DIAGONAL

(See paras. 2.27. and 2.29.)

| Variation of load capacity (per cent) |
| --- |
| Speed (km/h) | All load indices | Load indices ( 122 1/ | Load indices ( 121 1/ |
|  | Speed category symbol | Speed category symbol | Speed category symbol |
|  | F | G | J | K | L | M | L | M | N | P 2/ |
| 0 | +150 | +150 | +150 | +150 | +150 | +150 | +110 | +110 | +110 | +110 |
| 5 | +110 | +110 | +110 | +110 | +110 | +110 | +90 | +90 | +90 | +90 |
| 10 | +80 | +80 | +80 | +80 | +80 | +80 | +75 | +75 | +75 | +75 |
| 15 | +65 | +65 | +65 | +65 | +65 | +65 | +60 | +60 | +60 | +60 |
| 20 | +50 | +50 | +50 | +50 | +50 | +50 | +50 | +50 | +50 | +50 |
| 25 | +35 | +35 | +35 | +35 | +35 | +35 | +42 | +42 | +42 | +42 |
| 30 | +25 | +25 | +25 | +25 | +25 | +25 | +35 | +35 | +35 | +35 |
| 35 | +19 | +19 | +19 | +19 | +19 | +19 | +29 | +29 | +29 | +29 |
| 40 | +15 | +15 | +15 | +15 | +15 | +15 | +25 | +25 | +25 | +25 |
| 45 | +13 | +13 | +13 | +13 | +13 | +13 | +22 | +22 | +22 | +22 |
| 50 | +12 | +12 | +12 | +12 | +12 | +12 | +20 | +20 | +20 | +20 |
| 55 | +11 | +11 | +11 | +11 | +11 | +11 | +17.5 | +17.5 | +17.5 | +17.5 |
| 60 | +10 | +10 | +10 | +10 | +10 | +10 | +15.0 | +15.0 | +15.0 | +15.0 |
| 65 | +7.5 | +8.5 | +8.5 | +8.5 | +8.5 | +8.5 | +13.5 | +13.5 | +13.5 | +13.5 |
| 70 | +5.0 | +7.0 | +7.0 | +7.0 | +7.0 | +7.0 | +12.5 | +12.5 | +12.5 | +12.5 |
| 75 | +2.5 | +5.5 | +5.5 | +5.5 | +5.5 | +5.5 | +11.0 | +11.0 | +11.0 | +11.0 |
| 80 | 0 | +4.0 | +4.0 | +4.0 | +4.0 | +4.0 | +10.0 | +10.0 | +10.0 | +10.0 |
| 85 | -3 | +2.0 | +3.0 | +3.0 | +3.0 | +3.0 | +8.5 | +8.5 | +8.5 | +8.5 |
| 90 | -6 | 0 | +2.0 | +2.0 | +2.0 | +2.0 | +7.5 | +7.5 | +7.5 | +7.5 |
| 95 | -10 | -2.5 | +1.0 | +1.0 | +1.0 | +1.0 | +6.5 | +6.5 | +6.5 | +6.5 |
| 100 | -15 | -5 | 0 | 0 | 0 | 0 | +5.0 | +5.0 | +5.0 | +5.0 |
| 105 |  | -8 | -2 | 0 | 0 | 0 | +3.75 | +3.75 | +3.75 | +3.75 |
| 110 |  | -13 | -4 | 0 | 0 | 0 | +2.5 | +2.5 | +2.5 | +2.5 |
| 115 |  |  | -7 | -3 | 0 | 0 | +1.25 | +1.25 | +1.25 | +1.25 |
| 120 |  |  | -12 | -7 | 0 | 0 | 0 | 0 | 0 | 0 |
| 125 |  |  |  |  |  | 0 | -2.5 | 0 | 0 | 0 |
| 130 |  |  |  |  |  | 0 | -5.0 | 0 | 0 | 0 |
| 135 |  |  |  |  |  |  | -7.5 | -2.5 | 0 | 0 |
| 140 |  |  |  |  |  |  | -10 | -5 | 0 | 0 |
| 145 |  |  |  |  |  |  |  | -7.5 | -2.5 | 0 |
| 150 |  |  |  |  |  |  |  | -10.0 | -5.0 | 0 |
| 155 |  |  |  |  |  |  |  |  | -7.5 | -2.5 |
| 160 |  |  |  |  |  |  |  |  | -10.0 | -5.0 |

____________

1/	The load capacity indices refer to a single operation.

2/	Load variations are not allowed for speeds above 160 km/h.  For speed category symbols "Q" and above the speed category corresponding to the speed category symbol (see paragraph 2.28.2.) specifies the maximum speed permitted for the tyre.

# Footnotes

(/	Former title of the Agreement:

Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.

**/	For New Zealand, the date of entry into force is 21 April 2002.

(/	As defined in the Consolidated Resolution on the Construction of Vehicles (R.E.3) (document TRANS/WP.29/78/Rev.1).

/	See explanatory figure.

/	For consistency, the symbols and speeds shown in this table are the same as those for passenger cars (as in Regulation No. 30).  They should not be taken to indicate the speeds at which commercial vehicles fitted with such tyres may be operated on the roads.

/	Before 1 January 2000, the date of manufacture may be indicated by a group of three digits, the first two showing the week and the last one the year of manufacture.

/	This marking shall only be mandatory for tyre types approved to this Regulation after the entry into force of Supplement 14 to the Regulation.

/	1 for Germany, 2 for France, 3 for Italy, 4 for the Netherlands, 5 for Sweden, 6 for Belgium, 7 for Hungary, 8 for the Czech Republic, 9 for Spain, 10 for Serbia and Montenegro, 11 for the United Kingdom, 12 for Austria, 13 for Luxembourg, 14 for Switzerland, 15 (vacant), 16 for Norway, 17 for Finland, 18 for Denmark, 19 for Romania, 20 for Poland, 21 for Portugal, 22 for the Russian Federation, 23 for Greece, 24 for Ireland, 25 for Croatia, 26 for Slovenia, 27 for Slovakia, 28 for Belarus, 29 for Estonia, 30 (vacant), 31 for Bosnia and Herzegovina, 32 for Latvia, 33 (vacant), 34 for Bulgaria, 35 (vacant), 36 for Lithuania, 37 for Turkey, 38 (vacant), 39 for Azerbaijan, 40 for The former Yugoslav Republic of Macedonia, 41 (vacant), 42 for the European Community (Approvals are granted by its Member States using their respective ECE symbol), 43 for Japan, 44 (vacant), 45 for Australia, 46 for Ukraine, 47 for South Africa and 48 for New Zealand.  Subsequent numbers shall be assigned to other countries in the chronological order in which they ratify or accede to the Agreement Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions, and the numbers thus assigned shall be communicated by the Secretary-General of the United Nations to the Contracting Parties to the Agreement.

# Comments

PAGE 2 IS A BLANK PAGE

# Text boxes

issued by :		Name of administration:

......................................

......................................

......................................