| E/ECE/324 E/ECE/TRANS/505 |  | Rev.2/Add.105/Rev.1/Amend.1 |
| --- | --- | --- |
| 19 February 2010 |  |  |

# AGREEMENT

CONCERNING THE ADOPTION OF UNIFORM TECHNICAL PRESCRIPTIONS
FOR WHEELED VEHICLES, EQUIPMENT AND PARTS WHICH CAN BE FITTED
AND/OR BE USED ON WHEELED VEHICLES AND THE CONDITIONS FOR RECIPROCAL RECOGNITION OF APPROVALS GRANTED ON THE BASIS OF THESE PRESCRIPTIONS (/

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 105:  Regulation No. 106

## Revision 1 - Amendment 1

#### Supplement 7 to the original version of the Regulation - Date of entry into force: 24 October 2009

Uniform provisions concerning the approval of pneumatic tyres for agricultural vehicles and their trailers

_________

### UNITED NATIONS

Insert a new paragraph 3.1.8.1., to read:

"3.1.8.1.	The inscription 'I-3' for implement tyres with traction tread as identified in Annex 5, tables 5 and 6."

Insert a new paragraph 6.4.3., to read:

"6.4.3.	However, for the types of tyre for which the size designation is given in the first column of the tables in Annex 5, the allowed percentages are those given in the relevant tables, if any."

Annex 3, part C, amend to read:

"PART C: IMPLEMENT TYRES

Example of the markings to be borne by types of tyres

complying with this Regulation

250/70 R 20 IMP

MINIMUM HEIGHTS OF MARKINGS (mm)

...

(c)	the symbol "TUBELESS", I-3 if any, the optional word "RADIAL", the optional word "IMPLEMENT" and the date of manufacture may be at a distance from the size designation."

Annex 5,

Table 5, insert the following new tyre size designations:

"

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  | (mm) | (mm) | (mm) |
| 4.10/3.50-4 IMP | 2.10 | 89 | 272 | 101 |
| 190-8 IMP | 5.50 | 182 | 430 | 203 | " |

Table 5, insert a new column for "Overall diameter (D)" identified by (*), and add in the new column the relevant values for the following tyre size designations:

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  |  |  | (*) |  |
|  |  | (mm) | (mm) | (mm) |
| 4.00 – 8 IMP | 3 | 112 | 418 | 425 | 203 |
| 4.00 – 9 IMP | 3 | 112 | 443 | 460 | 229 |
| 4.0 – 10 IMP | 3 | 114 | 455 | 465 | 254 |
| 4.00 – 10 IMP | 3 | 114 | 465 | 475 | 254 |
| 4.00 – 12 IMP | 3 | 112 | 519 | 536 | 305 |
| 4.00 – 15 IMP | 3 | 112 | 595 | 612 | 381 |
| 4.00 – 18 IMP | 3 | 112 | 672 | 688 | 457 |
| 4.50 – 19 IMP | 3 | 124 | 720 | 733 | 483 |
| 4.80 – 8 IMP | 3,75 | 121 | 423 | 449 | 203 |
| 5.0 – 10 IMP | 4 | 145 | 505 | 517 | 254 |
| 5.00 – 12 IMP | 4 | 145 | 567 | 580 | 305 |
| 5.00 – 14 IMP | 4 | 145 | 618 | 631 | 356 |
| 5.00 – 15 IMP | 3 | 130 | 639 | 655 | 381 |
| 5.50 – 16 IMP | 4 | 150 | 685 | 703 | 406 |
| 5.90 – 15 IMP | 4 | 150 | 665 | 681 | 381 |
| 6.00 - 9 IMP | 4,5 | 169 | 543 | 556 | 229 |
| 6.00 – 16 IMP | 4 | 158 | 712 | 729 | 406 |
| 6.50 – 16 IMP | 4,5 | 173 | 735 | 754 | 406 |
| 6.70 – 15 IMP | 4,5 | 182 | 704 | 720 | 381 |
| 7.00- 12 IMP | 5 | 187 | 667 | 685 | 305 |
| 7.50 – 10 IMP | 6 | 214 | 634 | 649 | 254 |
| 7.50 – 16 IMP | 5,5 | 202 | 785 | 801 | 406 |
| 7.50 – 18 IMP | 5,5 | 202 | 836 | 852 | 457 |
| 7.50 – 20 IMP | 5,5 | 202 | 887 | 903 | 508 |
| 7.50 – 24 IMP | 5,5 | 202 | 989 | 1013 | 610 |
| 7.60 – 15 IMP | 5,5 | 193 | 734 | 751 | 381 |
| 13.50 – 16.1 IMP | 11 | 353 | 1021 | 1043 | 409 | " |

After table 5 (3 of 3), add the following notes to read:

"Notes:	1.	The suffix "IMP" may be replaced by the wording "IMPLEMENT" on the tyre sidewall.

2.	Tyres of radial structure are identified by means of the letter "R" in place of "-" (e.g. 7.5 L R 15).

3.	Overall diameters (D) in column (*) apply to tyres marked with classification 
code 'I-3' – see paragraph 3.1.8.2."

Table 6, insert a new column for "Overall diameter (D)" identified by (*), and add in the new column the relevant values for the following tyre size designations:

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  |  |  | (*) |  |
|  |  | (mm) | (mm) | (mm) |
| 8.5L – 14 IMP | 6 | 216 | 721 | 735 | 356 |
| 9.5L – 14 IMP | 7 | 241 | 741 | 757 | 356 |
| 9.5L – 15 IMP | 7 | 241 | 767 | 782 | 381 |
| 11L – 14 IMP | 8 | 279 | 752 | 770 | 356 |
| 11L – 15 IMP | 8 | 279 | 777 | 796 | 381 |
| 11L – 16 IMP | 8 | 279 | 803 | 821 | 406 |
| 12.5L – 15 IMP | 10 | 318 | 823 | 845 | 381 |
| 12.5L – 16 IMP | 10 | 318 | 848 | 870 | 406 |
| 16.5L – 16.1 IMP | 14 | 419 | 1024 | 1046 | 409 |
| 6.5/80 – 12 IMP | 5 | 163 | 569 | 588 | 305 |
| 6.5/80 – 15 IMP | 5 | 163 | 645 | 663 | 381 |
| 9.0/75 – 16 IMP | 7 | 226 | 749 | 770 | 406 |
| 10.0/80 – 12 IMP | 9 | 264 | 710 | 730 | 305 |
| 11.0/65 - 12 IMP | 9 | 281 | 670 | 692 | 305 |
| 10.0/75 - 15.3 IMP | 9 | 264 | 760 | 780 | 389 |
| 11.5/80 – 15.3 IMP | 9 | 290 | 845 | 867 | 389 |
| 10.5/80 – 18 IMP | 9 | 274 | 885 | 907 | 457 |
| 12.0/75 - 18 IMP | 9 | 299 | 915 | 937 | 457 |
| 12.5/80 - 18 IMP | 9 | 308 | 965 | 987 | 457 |
| 14.5/80 - 18 IMP | 12 | 372 | 1060 | 1082 | 457 |
| 15.0/55 - 17 IMP | 13 | 391 | 850 | 872 | 432 |
| 15.5/80 - 24 IMP | 13 | 394 | 1240 | 1262 | 610 |
| 16.0/70 - 20 IMP | 14 | 418 | 1075 | 1097 | 508 |
| 16.5/85 - 24 IMP | 13 | 417 | 1322 | 1344 | 610 |
| 16.5/85 - 28 IMP | 13 | 417 | 1423 | 1445 | 711 |

"

After table 6 (3 of 3), add the following note 3 to read:

3.	Overall diameters (D) in column (*) apply to tyres marked with classification 
code 'I-3' – see paragraph 3.1.8.2."

Table 7, insert the following new tyre size designations:

"

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  | (mm) | (mm) | (mm) |
| 13x6.00-6 | 5 | 154 | 330 | 152 |
| 14x4.50-6 | 3,5 | 113 | 356 | 152 |
| 18x7.50-8 | 6 | 191 | 457 | 203 |
| 19x9.50-8 | 7,5 | 240 | 483 | 203 |
| 20x8.00-8 | 6,5 | 204 | 508 | 203 |
| 20x9.00-8 | 7 | 227 | 508 | 203 |
| 21x7.00-10 | 5,5 | 177 | 533 | 254 |
| 23x9.50-12 | 7 | 235 | 577 | 305 |
| 24x12.00-12 | 9,5 | 304 | 610 | 305 |
| 25x8.00-12 | 6,5 | 203 | 635 | 305 |
| 25x10.00-12 | 8 | 254 | 635 | 305 |
| 25x11.00-12 | 9 | 279 | 635 | 305 |
| DH73x50.00-32 | 44 | 1270 | 1880 | 813 |

"

After table 7 (4 of 4), add the following note 4. to read:

"4.	Coefficient "b" for the calculation of the Overall diameter Dmax:

(a)	1.12 for tyres with Nominal rim Diameter (d) less than 380 mm;

(b)	1.10 for tyres with Nominal rim Diameter (d) 381 mm and above."

-----

# Footnotes

(/	Former title of the Agreement:

Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.

# Text boxes

2506