| E/ECE/324 E/ECE/TRANS/505 |  | Rev.2/Add.107/Amend.3 |
| --- | --- | --- |
| 11 May 2010 |  |  |

# AGREEMENT

CONCERNING THE ADOPTION OF UNIFORM TECHNICAL PRESCRIPTIONS
FOR WHEELED VEHICLES, EQUIPMENT AND PARTS WHICH CAN BE FITTED
AND/OR BE USED ON WHEELED VEHICLES AND THE CONDITIONS FOR RECIPROCAL RECOGNITION OF APPROVALS GRANTED ON THE BASIS OF THESE PRESCRIPTIONS (/

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 107:  Regulation No. 108

## Revision 2 - Amendment 3

#### Supplement 3 to the original version of the Regulation: Date of entry into force: 17 March 2010

Uniform provisions concerning the approval for the production of retreaded pneumatic tyres for motor vehicles 
and their trailers

_________

### UNITED NATIONS

Paragraph 1., amend to read (including the addition of footnote **/):

"1.	SCOPE

This Regulation covers the production of retreaded tyres designed primarily for vehicles of category M1, N1, O1 and O2. */ **/.  However, it does not apply to the production of:

1.1.	Retreaded tyres with a speed capability below 120 km/h or above 300 km/h;

1.2.	Tyres originally produced without speed symbols and load indices;

1.3.	Tyres originally produced without type approval and without either an "E" or "e" mark;

1.4.	Tyres designed for the equipment of cars produced prior to 1939;

1.5.	Tyres designed exclusively for competition or off road use and marked accordingly;

1.6.	Tyres designated as "T type" temporary use spares.

_______________

*/	As defined in Annex 7 to the Consolidated Resolution on the Construction of Vehicles R.E.3 (document TRANS/WP.29/78/Rev.1 as last amended by Amend. 4).

**/	This Regulation defines requirements for tyres as a component. It does not limit their installation on any categories of vehicles."

-----

# Footnotes

(/	Former title of the Agreement:

Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.