| E/ECE/324 E/ECE/TRANS/505 |  | Rev.2/Add.114/Amend.1/Corr.1 |
| --- | --- | --- |
| 6 March 2006 |  |  |

# AGREEMENT

CONCERNING THE ADOPTION OF UNIFORM TECHNICAL PRESCRIPTIONS
FOR WHEELED VEHICLES, EQUIPMENT AND PARTS WHICH CAN BE FITTED
AND/OR BE USED ON WHEELED VEHICLES AND THE CONDITIONS FOR RECIPROCAL RECOGNITION OF APPROVALS GRANTED ON THE BASIS OF THESE PRESCRIPTIONS (/

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 114:  Regulation No. 115

## Amendment 1 - Corrigendum 1

#### Corrigendum 1 to Supplement 1 to the original version of the Regulation, subject of Depositary Notification C.N.1276.2005.TREATIES-3 dated 21 December 2005

Uniform provisions concerning the approval of:

I	Specific LPG (liquefied petroleum gases) retrofit systems to be installed in motor vehicles for the use of LPG in their propulsion system

II.	Specific CNG (compressed natural gas) retrofit systems to be installed in motor vehicles for the use of CNG in their propulsion system

_________

### UNITED NATIONS

Paragraph 1.4., correct to read:

"1.4.	This Regulation applies to retrofit systems intended to be fitted on vehicles of categories M and N, with the exception of:

(a)	vehicles approved before the application of the requirements of Regulation No. 83, 01 series of amendments,

(b)	vehicles type-approved pursuant to Regulation No. 83, approval A and C,

(c)	vehicles type-approved pursuant to Regulation No. 83, others than M1 and N1 categories,

(d)	vehicles type-approved pursuant to Regulation No. 83, series of amendments 01 or 02 or 03 or 04 series,

(e)	vehicles type-approved pursuant to Regulation No. 49, series of amendments 01 or 02 or 03 series."

Insert a new paragraph 1.5., to read (footnote 1/ to the former paragraph 1.4. remains unchanged):

"1.5.	The requirements for the different categories (M1, N1 or others) are defined in paragraphs 2. to 7. 1/.

Once the retrofit system is installed in the vehicle, the modified vehicle shall fulfil all the provisions of the Regulation for which the type approval has been initially granted."

Paragraph 3.3., correct to read:

"3.3.	Installation manual(s) for the retrofit system installation on the parent vehicle(s)."

Paragraph 6.1.2.4., correct to read:

"6.1.2.4.	"Pollutants" means:

- carbon monoxide

(ii)	………….

…………"

Paragraphs 6.1.2.5.3.3. and 6.1.2.5.3.4., correct to read:

"6.1.2.5.3.3.	The ratios of CO2 emissions and fuel consumption shall be calculated as follows:

KCO2 = CO2LPG / CO2petrol

KCons = ConsLPG / Conspetrol

For each vehicle of the family, the official values of CO2 emissions are multiplied by the above ratios.

6.1.2.5.3.4.	Notwithstanding the provisions of paragraphs 6.1.2.5.3.1. and 6.1.2.5.3.2., for non intrusive system, as defined in paragraph 2.1.5. of this Regulation, the value of the petrol CO2 emission and the fuel consumption may be the official values of the vehicle No. i. "

Paragraph 6.1.3.4., correct to read:

"6.1.3.4.	Notwithstanding the provisions of paragraph 6.1.3.1., with regard to the way to calculate the mean of maximum power on petrol in paragraphs 6.1.3.2. and 6.1.3.3., for non intrusive system, as defined in paragraph 2.1.5. of this Regulation, the value of maximum power on petrol of the vehicle No. i may be the official value."

Paragraph 6.1.4.1.2., correct to read:

"6.1.4.1.2.	"LPG emission-related component" means any component in the air inlet or in the exhaust system which supplies an input to or receives an output from the LPG controller."

Paragraph 6.2.2.4., correct to read:

"6.2.2.4.	"Pollutants" means:

(i)	carbon monoxide

(ii)	……………….

………………"

Paragraphs 6.2.2.5.3.3. and 6.2.2.5.3.4., correct to read:

"6.2.2.5.3.3.	The ratios of CO2 emissions and fuel consumption shall be calculated as follows:

KCO2 = CO2CNG / CO2petrol

KCons = ConsCNG / Conspetrol

For each vehicle of the family, the official values of CO2 emissions and fuel consumption are multiplied by the above ratios.

6.2.2.5.3.4.	Notwithstanding the provisions of paragraphs 6.2.2.5.3.1. and 6.2.2.5.3.2., for non intrusive system, as defined in paragraph 2.1.5. of this Regulation, the value of the petrol CO2 emission and the fuel consumption may be the official values of the vehicle No. i. "

Paragraph 6.2.4.1.2., correct to read:

"6.2.4.1.2.	"CNG emission-related component" means any component in the air inlet or in the exhaust system which supplies an input to or receives an output from the CNG controller."

Paragraphs 7.1.3.5. to 7.1.3.7., correct to read:

"7.1.3.5.	The installation manual can be divided in two parts:

Part I:	(i)	Part containing the description of the sample of the retrofit system.

(ii)	Part containing the list of components indicated by the retrofit manufacturer as alternatives.

Part II:	(i)	Part containing installation instructions for the specific vehicle.

7.1.3.6.	Installation manual of the parent vehicle(s) has to be submitted to the authority that grants the type approval.

7.1.3.7.	Installation manual of the vehicles belonging to the family has to be filed by the retrofit system manufacturer for a time to be determined in accordance with the authority that grants the type approval."

Annex 1A – Addendum, item 3., correct to read:

"3.	Vehicles type(s) for which the retrofit equipment type is qualified:

| Fuel | Petrol (or diesel) 1/ | LPG |
| --- | --- | --- |
| Vehicle type | Engine type | Power (kW) | CO 3/ (g/km) | HC 3/ (g/km) | NOx 3/ (g/km) | CO2 2/ (g/km) | Power (kW) | CO 3/ (g/km) | HC 3/ (g/km) | NOx 3/ (g/km) | CO2 2/ (g/km) |

1/	Strike out what does not apply.

2/	Applicable to vehicles of category M1 and N1 only.

3/	Applicable only to parent vehicle(s)"

Annex 1B - Addendum, item 3., correct to read:

"3.	Vehicles type(s) for which the retrofit equipment type is qualified:

| Fuel | Petrol (or diesel) 1/ | CNG |
| --- | --- | --- |
| Vehicle type | Engine type | Power (kW) | CO 3/ (g/km) | HC 3/ (g/km) | NOx 3/ g/km) | CO2 2/ (g/km) | Power (kW) | CO 3/ (g/km) | HC 3/ (g/km) | NOx 3/ (g/km) | CO2 2/ (g/km) |

1/	Strike out what does not apply.

2/	Applicable to vehicles of category M1 and N1 only.

3/	Applicable only to parent vehicle(s)"

-----

# Footnotes

(/	Former title of the Agreement:

Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.