|  |  | ECE/TRANS/180/Add.3/Corr.3 |
| --- | --- | --- |
|  |  | 21 October 2010 |

Global registry

Created on 18 November 2004, pursuant to Article 6 of the Agreement concerning the establishing of global technical regulations for wheeled vehicles, equipment and parts which can be fitted and/or be used on wheeled vehicles (ECE/TRANS/132 and Corr.1) done at Geneva on 25 June 1998

Addendum 3: Global technical regulation No. 3

Motorcycle brake systems

Corrigendum 2

Established in the Global Registry on 23 June 2010

_______________

UNITED NATIONS

Paragraph 3.3.1., amend to read:

“3.3.1.		MFDD (Mean fully developed deceleration):

Calculation of MFDD:

|  | m/s2 |
| --- | --- |

Where:

dm	= mean fully developed deceleration

Vb	= vehicle speed at 0.8 V1 in km/h

Ve	= vehicle speed at 0.1 V1 in km/h

Sb	= distance travelled between V1 and Vb in metres

Se	= distance travelled between V1 and Ve in metres

V1	= vehicle speed when rider actuates the control”

Paragraph 4.1.1.3., amend to read:

“4.1.1.3.	Measurement of PBC:

The PBC is measured as specified in national or regional legislation using either:

(a)	The American Society for Testing and Materials (ASTM) E1136 – 93 (Re-approved 2003) standard reference test tyre, in accordance with ASTM Method E1337-90 (Re-approved 2002), at a speed of 40 mph; or

(b)	…”