|  |  | ECE/TRANS/180/Add.6/Amend.1 |
| --- | --- | --- |
|  |  | 6 April 2011 |

Global registry

Created on 18 November 2004, pursuant to Article 6 of the Agreement concerning the establishing of global technical regulations for wheeled vehicles, equipment and parts which can be fitted and/or be used on wheeled vehicles (ECE/TRANS/132 and Corr.1) done at Geneva on 25 June 1998

Addendum 6: Global technical regulation No. 6

Safety glazing materials for motor vehicles and motor vehicle equipment

Amendment 1

Established in the Global Registry on 9 March 2011

_______________

UNITED NATIONS

Paragraphs 4.1.2.1. to 4.1.2.3.3, amend to read:

"4.1.2.1.	Identification marks for windscreens.

4.1.2.1.1.	"II" for laminated-glass.

4.1.2.1.2.	"IV" for glass-plastics.

4.1.2.2.	Identification marks for panes.

4.1.2.2.1.	No symbol is required for uniformly toughened glass.

4.1.2.2.2.	"XI" for laminated glass.

4.1.2.2.3.	"VI" for a double glazed unit.

4.1.2.2.4.	"XII" for glass-plastics.

4.1.2.3.	Additional identification marks.

4.1.2.3.1.	Glazing faced with plastic shall be marked with "/P" after the mark required by paragraph 4.1.2.1. or 4.1.2.2., e.g., II/P.

4.1.2.3.2.	Glazing with a light transmission of less than 70 per cent shall be marked with "/V" and the mark required by paragraph 4.1.2.2.

4.1.2.3.3.	If glazing requires both the "/P" and the "/V", the mark required by paragraph 4.1.2.3.1 shall precede the mark required by paragraph 4.1.2.3.2."