Informal document No. 15

81st GRSG, 9-11 October 2001

agenda item 7

# Regulation No. 39 – Speedometer equipment

## Trasmitted by the expert from Italy

In order to assess whether or not the “on road “test and the roller test are equivalent , even with a reduced roller diameter, some tests have been carried out on different types of motorcycles

| Tested Model | Real speed (km/h) (1) | Speed indicated by the speedometer Test on the road (km/h) | Speed indicated by the speedometer Test on the roller (km/h) (2) |
| --- | --- | --- | --- |
| A: 100 cc | 40 65 | 42 73 | 42 73 |
| B: 650 cc | 40 80 120 | 45 88 130 | 45 88 130 |
| C: 1000 cc | 40 80 120 | 41 82 122 | 40 81 121 |

(1) measured with an optical sensor Datron, model DSL 1

(2) diameter 502 mm  width= 600 mm  power 110 kw

The test results show that there is equivalence between the two methods (on the road and on dynamometer roller

Therefore the use of a dynamometer roller with a reduced  diameter is supported by Italy