# IHRA Side Impact Working Group Status Report 
GRSP, December 2001

# What is IHRA?

## International Harmonised Research Activities formed at 15th ESV in Melbourne during 1996

## International government steering committee

## 6 Working Groups to coordinate research in 6 major problem areas of road safety

# What is IHRA?

## Vehicle Compatibility (UK/EEVC)

## Advanced Offset Frontal (Italy, EEVC)

## Biomechanics (NHTSA/USA)

## Pedestrian Safety (JMoT, Japan)

## Intelligent Transport Systems (Transport Canada)

## Functional Equivalence (USA/ Australia)

# IHRA Side Impact Working Group

## Side Impact Working Group formed after 1998 ESV

### to replace Functional Equivalence

### lead country Australia

## SIWG held its first meeting in Gothenburg in September 1998.

# IHRA Side Impact Working Group

## Side Impact Working Group has around 10 members

### enhances likelihood of progress

## Governments of Europe, USA, Canada, Australia and Japan represented.

## 3 Industry experts from OICA

### one each from North America, Europe and Asia-Pacific

# SIWG - Terms of Reference

## The terms of reference of the SIWG is to co-ordinate research worldwide to support the development of future side impact test procedure(s) to maximise harmonisation with the objective of enhancing safety in real world side crashes.

# SIWG - Terms of Reference

## Real world crash studies to define problem

## Protect both front and rear adult and child occupants

## Interact with IHRA Biomechanics, Offset frontal and compatibility WG

## Involved in development of WorldSID or other side impact dummy

## Examine component or sub-systems tests

# Real World Crash Studies

## Vehicle-to-vehicle and vehicle to narrow object crashes - 90% side impact trauma

## Most trauma to struck side

## up to 40% trauma to non-struck side

## Head and chest most frequent

## Abdominal, pelvic and lower extremities

## Contacts - B-pillar, door, exterior object

# Real World Crash Studies

## Females predominated in vehicle-to-vehicle crashes (up to 60%)

## Males predominated in vehicle-to-narrow object crashes

## Elderly over-represented in vehicle-to-vehicle crashes

## Rear occupants < 15% of side impact trauma

# Interaction with Other Researchers

## Outcome of accident studies related to  IHRA Biomechanics and WorldSID Task Group

## Defined what needed to be measured to guide WorldSID design

## IHRA Biomechanics to provide anthropometry, biofidelity requirements and injury criteria

# Interaction with Other Researchers

## IHRA Frontal and Compatibility WGs kept informed on progress of side impact WG

## Interaction expected to become more formalised as test procedures become more crystallised

## Need to ensure that countermeasures in one area do not degrade safety in another

# WorldSID

## IHRA Biomechanics provided anthropometry for 50% male

## Australia hosted workshop to launch prototype WorldSID in December 2000

### SIWG meeting held back-to-back

## SIWG requested development of 5% female WorldSID

# Proposed Test Procedures

## Accident data indicated 4-part test procedure required:

### Mobile Deformable Barrier to vehicle test

### Vehicle to pole test

### Out-of-position side airbag evaluation

### Sub-systems head impact test

# Mobile Deformable Barrier Test

## Most challenging task for the group

## Injury outcome in first 40 msec

## Intrusion not good predictor of injury

## Parametric studies to examine effect of mass, stiffness & geometry on injury outcome

# MDB Test - Main Issues

## Need for rear dummy?

## Crabbed or perpendicular test?

## Barrier element - homogeneous or not?

## Stiffness distribution of barrier element?

## Mass of trolley?

## Ground clearance of barrier?

## Non-struck side test?

# MDB Test - Stiffness/Homogeneity

## Stiffness distribution determines intrusion profile shape

## Are current elements representative of current fleets?

## Is only initial stiffness important?

### little crush of bullet vehicle

### issue for compatibility

# MDB Test - Kerb Mass

## European/Japanese fleet average mass of passenger cars is 1150-1200 kg

## US passenger car fleet 1415 kg

## US LTV fleet 1920 kg

## US Pass car/LTV fleet 1635 kg

## Europe may consider 1500 kg

### US and Japan undecided

# MDB Test - Ground Clearance

## US want something representative of LTVs

### perhaps 450 mm

## Rest of world will consider 350 mm

## Perhaps 350 mm ground clearance plus mandating “blocker beams” in LTVs

# MDB Test - Agreed Points

## Longitudinal impact velocity component of 50 km/h

## Small adult female driver dummy.

## Seatbelts applied

# Pole Test

## Moving vehicle to pole test

## Perpendicular impact

## Impact speed 30 km/h

## Evaluate head and thorax(at least)

## Mid size male

## Rigid pole [350 mm]

### load head and thorax simultaneously

# Out-of-position side airbag evaluation

## ISO TR 14933, NHTSA and Transport Canada and IIHS research

## NHTSA and Transport Canada to review current research

# Sub-Systems Head Impact Test

## Based on FMVSS 201

## Also new research from EEVC

# Future of IHRA

## Future of IHRA discussed at 17th ESV

## Support for IHRA to continue

## Governments must be prepared to provide IHRA specific resources

## Governments must be prepared to develop IHRA outcomes into harmonised regulations

# Future of IHRA SIWG

## Terms of Reference currently being revised to reflect progress to date and what needs to be done to complete task (copy attached)

## To include research into non-struck side injuries

## ISO to develop small female version of WorldSID

### seeking funding

# Future of IHRA SIWG

## Plan to have test procedures fully drafted in time for 18th ESV in Japan in 2003

## Plan to coordinate evaluation of these test procedures by 2005 ESV

# IHRA SIDE IMPACT WORKING GROUP:

# NEW TERMS OF REFERENCE (2001 – 2005)

# Objective

Co-ordinate research worldwide to support the development of future side impact test procedure(s) to maximise harmonisation with the objective of enhancing safety in real world side crashes.

# Scope

In its first 2-year term, the Side Impact Working Group (SIWG) concluded that new test procedures to address the side impact problem should include:

- A mobile deformable barrier to vehicle test

- A vehicle to pole test

- Out of position airbag evaluation

- Sub-systems head impact test

In its next term, the SIWG will also coordinate research to examine the feasibility of improving side impact protection for occupants on the non-struck side and develop a test procedure to evaluate such protection.

# Activities

The SIWG is working towards achieving these goals by:

- Reviewing any new real world crash data to prioritise injury mechanisms and identify associated crash conditions taking into account likely future trends.

- Taking into account the need to protect both front seat and rear seat(s) adult and child occupants.

- Interaction with the IHRA Biomechanics Working Group to monitor the development of harmonised injury criteria.

- Interaction with the IHRA vehicle compatibility working group to ensure solutions in one area do not degrade safety in another.

- Monitoring and, as appropriate, providing input to the development of WorldSID and any other side impact dummy.

- Determining the greatest degree of harmonisation feasible and the design and vehicle safety performance implications of adopting different levels of test severity or the worst case condition.

- Coordinating the evaluation of proposed test procedures subject to availability of test dummies and injury criteria.

# Timeframe

While the progress of the group will be reviewed every 2 years, it is expected that:

- The target date for draft final proposal of test procedure(s) is 2003 ESV

- The target date for final proposal of test procedure(s) is 2005 ESV.